## Slide 1
Quantum Random Number Generation
Chaganti Kamaraja Siddhartha
EP20B012
Project Guide: Prof. Bijoy Krishna Das
EE4901:Mini-Project Jan-May 2024
Dept. of Electrical Engineering
IIT Madras
Outline
Overview
Motivation
Experimental setup
Noise characterisation
Post processing
Real time bit stream generation
Discussion
Applications

## Slide 2
LASER
1550nm
50:50
Beam Splitter
ADC + FPGA
Computer
Balanced
Photodetector
Bit-stream
Extracted Noise
Signal (analog)
Vacuum
TIA
Experimental Setup

## Slide 3
1550 nm
Laser
Optical
inputs
Optical
outputs
Beam splitter
PD
PD
SUB
Extracted Noise signal

## Slide 5
Post-processing
000
001
010
011
100
101
110
111

## Slide 6
LASER
1550nm
50:50
Beam Splitter
DSO
Computer
Balanced
Photodetector
Samples
Extracted Noise
Signal (analog)
Vacuum
TIA
Experimental Setup with DSO

## Slide 7
Post processing with DSO
50 MSPs
500 MSPs
Passed 12/15 tests
Passed 11/15 tests
150,000 bits are tested using NIST test suite

## Slide 8
Post processing with DSO
50 MSPs
500 MSPs
Passed 12/15 tests
Passed 11/15 tests
150,000 bits are tested using NIST test suite
100 Megabits are needed to test NIST test suite

## Slide 9
Bit-stream generation with FPGA
Data of starting 1 hour is ignored in quantiles calculation.
Normal distribution
Variation of quantiles w.r.t time
1.6 Lakh samples (chunk) acquired at 31.25 MSps
30 chunks for every 10 min.
Repeated for 5 hours

## Slide 10
200 Megabits are generated
Avg. Speed of 20 Kbps
Bits arrive at different time intervals
Bit-stream generation
Bin proportion

## Slide 11
Real time Bit-streaming
Time difference between two consecutive bits
Bits should arrive at equal intervals for QKD applications
10,000 bits are received at a time interval of 0.1 0.01 s
10,000 bits are received at a time interval of 0.1 ± 0.01 s
Speed = 10 bits/s
Bits should arrive at equal intervals for QKD applications
Speed = 10 bits/s

## Slide 12
Future Work
PIC is used in place of optical fibre
Improve speed of real time bit stream
Quality check of Random bits using NIST test suite

## Slide 13
Overview
Why Quantum is needed to generate random numbers?
  Motivation
What is Quantum in Quantum Random Number Generator?
  Experimental setup
  Noise characterisation
How is Quantum noise used to generate random numbers?
  Post processing
  Real time bit stream generation
  Discussion
Where is Quantum Random Number generator used?
  Applications

## Slide 14
God doesn’t play dice with the universe
Not only does god play dice, but… he sometimes throws them where they cannot be seen.
Motivation
AI generated cartoon of Albert Einstein and Stephen Hawking
Quantum theory is probabilistic!!

## Slide 15
7Kb/s
Red pitaya has a ram of 512 MB.
Clock speed of DDR3 is 557 MHz .
Around Half million samples are used to determine the quantile cuts.
150 million bits are transferred to computer using TCP/IP protocol.
TCP/IP protocol is used to send bit stream real time
Post processing Real time

## Slide 16
Noise Characterization

## Slide 17
Experimental Setup

## Slide 18
DSO Experimental Setup

## Slide 19
Quantization of samples into bins
Variation of median of samples as time progress
Discussion

## Slide 20
Applications
Quantum Key Distribution